## Slide 1: TDS measuring protocol
Use a reliable TDS meter
If unceration, ask a Bluewater technician for guicance.
Draw water from the correct sampling point
Take the water sample from the Bluewater faucet. If not possible, the next best point is directly from the pressureless tank
Do not sample from an espresso machine
Machine piping can introduce other particles
Always draw at least 1 liter of water
This ensures the dosing is active and stable for measurement.
Only measure cold water
Heated water can cause inaccurate readings due to dissolved gases and mineral behavior changes.
1
2
3
4
5
Important note:
TDS is about adding up numbers. If the purifier is letting through 10 or 20 ppm, that is added to the ppm of the mineral dosing. If TDS is inconsistent after mineralisation, please measure the purified water before mineralisation as well.